## Slide 1: Fast Plant Classification in a Robotic Application
Master Thesis Presentation
- Priya Konda

## Slide 2: Contents
Introduction
Flow Chart
Dataset Preparation
Transfer Learning
Model Re-training
Training Loop
Nvidia Jetson Nano
TensorRT
Image Processing
The Robot
ROS Computational Graph
Results

## Slide 3: Introduction
Deep learning in everyday life
Classification, Detection, Segmentation
Ex: Smartphone applications (Translator, Face detection)
Classification: Identifies the correct class based on training dataset.
Uniqueness in features of flower and leaf.
Goal: Practically witness the classification process on a robotic application

## Slide 4: Flow Chart

## Slide 5: Dataset Preparation
Geranium and Azalea
Balanced dataset
Folder Structure
Images at different angles and position.

## Slide 6: Transfer Learning
Fine Tuning By default requires_grad == True Train all the layers
Fixed Feature Extractor Freeze Initial Layers, requires_grad == False Train the last layer
Torchvision Library model = models.resnet50(pretrained=True)
The image dimensions should match the pre-trained model.

## Slide 7: Model Re-training
Quadro P620 and GeForce RTX 2070
alexnet, vgg16, resnet50
Data Augumentation. (flip, crop, resize)
Batch_Size = 4
Train mode - model.train()
Evaluation mode - model.eval()
Trained for 30 epochs
Evaluation using metrics
Saved the model in .pth format
The model is than converted to ONNX format using torch.onnx.export

## Slide 8: Training Loop
Forward Pass : Prediction output = model(inputs)
Backward Pass : Loss , Optimizer criterion = nn.CrossEntropyLoss() loss = criterion (outputs, labels) optimizer = optim.SGD(parameters(), lr=0.001, momentum=0.9) Loss.backward()
Update the weights optimizer.step()
Empty the gradients optimizer.zero_grad()

## Slide 9: Nvidia Jetson Nano
USB drive, Display and HDMI Port, 5V battery, Ethernet, 4GB RAM, SD card slot.
Nvidia jetpack SDK is flashed on the SD card
Pre-installed software tools
Deploying Deep Learning Repository
Deep Learning Nodes for ROS/ROS2 Repository
DNN Vision library
Image source: https://developer.nvidia.com/embedded/jetson-nano-developer-kit

## Slide 10: TensorRT
Image source: https://docs.nvidia.com/deeplearning/tensorrt/developer-guide/index.html
Programmable Inference Acceralator
TensorRT Optimizer Trained model Precision Calibration: float32, float16 or int8
Fix Batch Size
TensorRT Runtime Engine
Storing the Engine file in disk - Serialize
Loading the engine file from memory - Deserialize

## Slide 11: Image Processing
Speed: Feature Based Method > Deep learning method
Contours on Images
Image Thresholding, Canny Edge Detection
cv2.arcLength, cv2.approxPolyD
Masking the red colour on Images cv2.cvtColor(image, cv2.COLOR_BGR2HSV)
Lower and upper bound is in range, mask=cv2.inRange(image, lower, upper)
Threshold value to grab frame, cv2.countNonZero(mask)

## Slide 12: Image Processing

## Slide 13: The Robot
Raspberry Pi 4
BeagleBone Blue
Logitech Camera
Batteries
Display screen
Ultrasonic sensors
Standard Wheels
Esp32

## Slide 14: The working

## Slide 15: ROS Computation Graph
Node names
Subscribers
Publishers
ROS msgs

## Slide 16: Results
resnet50
alexnet
vgg16

## Slide 17: Results
resnet50
alexnet
vgg16

## Slide 18: Results

## Slide 19: THANK YOU
Prof. Dr.-Ing. Franz Brümmer
Prof. Dr. Jörg Eberhardt
Mr. Torsten Schoder